BOSCH Motronic Fault Codes (Rev1)

Fault Code / Item				Abbreviation		Recorded Fault
 
12 Diagnosis Initiated 						n/a
13 Lambda (Oxygen) Sensor 					No Voltage Change – Open Ckt.
14 Coolant Temperature Sensor 		CTS			Voltage Low
15 Coolant Temperature Sensor 		CTS			Voltage High
16 Knock Sensor 1 							No Voltage Change

17 Knock Sensor 2 							No Voltage Change
18 Knock Control Unit 			KCU			No Signal, ECU Fault
19 Crankshaft Sensor 						Incorrect Signal
21 Throttle Position Sensor 			TS			Voltage High
22 Throttle Position Sensor 			TS			Voltage Low
23 Knock Control Module 						n/a
24 Vehicle Speed Sensor 			VSS			No Signal
25 Injector Valve 1 							Voltage High
26 Injector Valve 2 							Voltage High
27 Injector Valve 3 							Voltage High
28 Injector Valve 4 							Voltage High
29 Injector Valve 5 							Voltage High
31 Crankshaft Angle Sensor (RPM)		CAS			No Signal 
32 Injector Valve 6 							Voltage High
33 Exhaust Gas Recirculation Valve		EGR			Voltage Low
34 Exhaust Gas Recirculation Valve		EGR			Voltage High
35 Idle Speed Control Valve 			ISCV			Poor Or No Idle Speed Control
37 Fault Code Light							Voltage Low
38 Lambda (Oxygen) Sensor						Voltage Low
39 Lambda (Oxygen) Sensor 					Voltage High
41 Vehicle Speed Sensor 			VSS			Voltage Low
42 Vehicle Speed Sensor 			VSS			Voltage High
44 Lambda (Oxygen) Sensor 					Weak Mixture
45 Lambda (Oxygen) Sensor						Rich Mixture
46 Air Pump Relay 							Voltage High
47 Air Pump Relay 							Voltage Low
48 Battery								Voltage Low 
49 Battery 								Voltage High 
51 Electronic Control Unit			ECU			PROM Error/Hardware Failure
52 Fault Code Light 							Voltage High
53 Fuel Pump Relay (Main Relay)					Voltage Low
54 Fuel Pump Relay (Main Relay)					Voltage High
55 Electronic Control Unit 			ECU			Hardware Failure- Unit Fault
56 Idle Speed Control Valve			ISCV			Voltage High
57 Idle Speed Control Valve 			ISCV			Voltage Low
59 Inlet Manifold Valve 1 						Voltage Low
61 Fuel Tank Vent Valve 			FTVV			Voltage Low
62 Fuel Tank Vent Valve			FTVV			Voltage High
63 Inlet Manifold Valve 1 						Voltage High		Repeat?

63 EST Line Coil Cylinder 2&3 (M2.8/XEV systems)			Voltage Low		Repeat?

64 EST Line Coil Cylinder 1&4 (M2.8/XEV systems)			Voltage Low
65 Carbon Monoxide (Co) Potentiometer				Voltage Low
66 Carbon Monoxide (Co) Potentiometer				Voltage High

67 Throttle Valve Switch – Idle Position Switch			Voltage Low - Not opening
68 Throttle Switch – Idle contact		TS			Idle Switch Not Opening
69 Air Temperature Sensor			ATS			Voltage Low
71 Air Temperature Sensor			ATS			Voltage High
72 Throttle Switch – Full Load Contact	TS			Not Opening 
73 Air Flow Sensor				AFS			Voltage Low
74 Air Flow Sensor				AFS			Voltage High
75 Auto Transmission Torque Control	AT			Voltage Low
76 Auto Transmission Torque Control	AT			Engaged Long/Ignition Retard

79 Traction Control				TC			Incorrect Ignition/Injector CutOff
81 Injector Valve 1							Voltage Low
82 Injector Valve 2							Voltage Low
83 Injector Valve 3							Voltage Low
84 Injector Valve 4							Voltage Low
85 Injector Valve 5							Voltage Low
86 Injector Valve 6							Voltage Low
87 Air Conditioning Cut-off Relay		AC			Voltage Low
88 Air Conditioning Cut-off Relay		AC			Voltage High
89 Lambda (Oxygen) Sensor Heater					Voltage Low
91 Lambda (Oxygen) Sensor Heater 				Voltage High
92 Camshaft Sensor (XEV Systems)					Incorrect Signal
93 Hall Effect Sender 				HES			Voltage Low
94 Hall Effect Sender				HES			Voltage High

95 Hot Start Valve							Voltage Low

96 Hot Start Valve							Voltage High
97 Traction Control				TC			Incorrect Signal
98 Lambda (Oxygen) Sensor						Open Circuit – Wiring Break
113 Boost Pressure Control						Boost Too High - Out Of Range
114 Boost Pressure Idle						Above Upper Limit
115 Boost Pressure Full						Below Lower Limit
116 Boost Pressure							Above Upper Limit
117 Waste Gate Valve						Voltage Low
118 Waste Gate Valve						Voltage High
121 Lambda (Oxygen) Sensor 2					Lean Exhaust - Weak Mixture
122 Lambda (Oxygen) Sensor 2					Rich Exhaust - Rich Mixture
123 Inlet Manifold Valve 1						Blocked
124 Inlet Manifold Valve 2						Blocked
132 Exhaust Gas Recirculation Valve	EGR			Incorrect Signal
133 Exhaust Gas Recirculation Valve 2	EGR 			Voltage High
134 Exhaust Gas Recirculation Valve 2	EGR 			Voltage Low
135 Fault Code Light 							Voltage Low
136 Electronic Control Unit 			ECU			n/a
137 Electronic Control Unit Case 		ECU			High Temperature
141 Secondary Air Pump						Not Enough Air
142 Secondary Air Pump						Air Without Pump
143 Immobiliser Function In ECU 					No Or Incorrect Signal
144 No Immobiliser Signal Received					Faulty Unit Or Break In Wiring
145 Incorrect Immobiliser Signal Received				Faulty Unit Or Break In Wiring