7 Network Topologies

| 1 | What is the main characteristics of a local area network (LAN) |
| --- | --- |
|  | a) High data transfer rate b) Low error rate c) Over short distance (within building) |
| 2 | Identify some of the functions/advantage of local area network? |
|  | a) Share resources :As servers (printers and files ) b) Share resources : applications and databases c) Allow for users on system to communicate (chat, email, text) |
| 3 | Identify some of the areas when LAN is useful. |
|  | a) In academic institution within the classroom for teaching b) In factories for supporting manufacturing process. c) As administrative supports in all types of offices (database, accounting, personnel ) |
| 4. | What are 3 basic types of network topologies? |
|  | a) bus b) ring and c) star |
| 5 | Describe the “bus network” (Ethernet). |
|  | It consists of a central cable which forms the backbone or “bus”. All devices (workstation, servers and printers) are connected to this common bus. |
| 6 | How is data transmitted along the bus network? |
|  | Each device on the bus network has an address. All devices will listen to the bus to sense whether there is a transmission of data on the bus. Device A transmit to device B during a “free slot”a when no users are transmitting.. Device B listening to the bus, will pick up the data. All other devices will ignore the data. If 2 devices transmit at the same time, a collision occurs. The data packet will have to be re-transmitted again by the 2 devices at a later moment. This scheme is called Carrier Sense Multiple Access /Collision Detect (CSMA/CD) |
| 6 | What is the advantage of the bus network? |
|  | a) Inexpensive (less cable) b) easy to install c) additional stations can be added easily |
| 7 | What is the disadvantage of bus network? |
|  | a) Break in bus cable will cause network failure. b) Heavy traffic will caused too much collision and degrade the network. c) Errors difficult to trouble shoot. |
| 8 | What is the ring topology? |
|  | All devices are connected to one another in the shape of a closed loop. Each device is connected to two other devices on the ring. |
| 9 | How is data transmitted in a ring network? #20 |
|  | Tokens (blocks of data) are passed round the ring in one direction. Each token may be empty or may contain a packet of data.. Each station acts as a repeater and pass the token to the next station. Station AA may put a packet of data into an empty token and addressed it to station BB The token will travel round the ring and station BB will pick up the data. |
| 10 | What is the advantages and disadvantages of ring topology? |
|  | -higher transmission rate -span larger distances -Breakdown at a node will disable the ring -Difficult to install |
| 11 | Describe a star network # 24 |
|  | All devices or workstations are connected to a central computer or hub. |
| 12 | What are the advantages and disadvantages of a star network? |
|  | -Failure of one computer will not affect the network. -Easy to add a new device to central hub -Network does not degrades like bus with more sets. -Relatively expensive because more cabling.. -Failure of hub or central computer will cause failure of network |
| 13 | What is a bridge? |
|  | A bridge connects 2 local area network |
| 14 | What is a gateway/router? |
|  | WAN are connected by routers or gateway. A gateway is a computer that act as a bridge between different networks. |